## Slide 1: Aerospace Control Systems Exam Project
Prof. Marco Lovera
Caironi Giacomo 10778766
Caccia Riccardo 10811815
A.Y. 2024-2025
Robust control of the lateral dynamics of a multirotor UAV

## Slide 2: Introduction
Assignement Overview
System Model
Performance Requirements
Closed-Loop Analysis
Robust Stability
Robust Performance
Montecarlo Analysis
Conclusions

## Slide 3: Assignement Overview
The ANT-X quadrotor is a small quadrotor drone designed for research and education.
Grey-box models of ANT-X have been identified from flight test data and are available for control law design.
The project task is to design and verify a robust single-axis attitude control system for the ANT-X quadrotor.

## Slide 4: System Model

## Slide 5: System Model
Uncertainties are given in terms of standard deviations (provided as percentage of corresponding nominal values)
To ensure robustness of stability for model uncertainty associated with ranges on all parameters, uncertainties are defined using the following percentage with a normal distribution from ureal

## Slide 6: System Model – Poles and Zeros

## Slide 7: System Model – Bode Plot

## Slide 8: System Model – Step Response

## Slide 9: System Model - Closed Loop
The controller used for the lateral dynamics of the quadrotor is composed by a P - PID cascade
where the outer proportional controller for the roll angle R𝜑(𝑠) is:
p0 =𝐾𝜑𝑒𝜑 with 𝑒𝜑 = 𝜑0− 𝜑
and the inner PID controller for the roll rate 𝑅𝑝(𝑠) is:
with 𝑇𝑝=0,02 s 𝑒𝑝 = P0 − P

## Slide 10: Performance Requirements
Nominal performance: response of 𝜑 to variations in 𝜑0 equivalent to a second order response with 𝜔𝑛 ≥ 10 rad/s and 𝜉 ≥ 0.9.
Control effort limitation: |𝛿𝑙𝑎𝑡| ≤ 0.05 fo for a given doublet change in 𝜑0 (with 10*(π/180) rad amplitude) given by 
Robust stability: ensure robustness of stability to model uncertainty associated with ranges on all parameters, treated as deterministic bounds (this will be analyzed separately)

## Slide 11: Performance Requirements - Nominal Performance
Compute the settling time and the percentage of overshoot of our desired approximated second order complementary sensitivity transfer function

## Slide 12: Performance Requirements – Nominal Performance
Design of the performance weight Wp(s) that will be used in the H synthesis
the aim is to employ it for shaping the sensitivity function to meet the specified performance criteria, since H condition is known
Where M is related to the peak, A is related to the value at steady state and ωp is related to the cross-over frequency and so to the settling time of our response.

## Slide 13: Performance Requirements – Nominal Performance
But remembering the fundamental identity
If as we said
in other words, the actual complementary sensitivity function should at least match or exceed the behavior of the target function

## Slide 14: Performance Requirements – Control Effort
the weight on control sensitivity has the important function to keep the control action moderated; indeed, in practice control action is provided by actuators, which have limited control authority both in range and rate; also, the actuator bandwidth is limited.
as did before, the performance weight must be designed and then will be used in the H synthesis.
where act is related to the frequency of the actuators, while represent the high frequency gain of the weight

## Slide 15: Performance Requirements – Control Effort
For a doublet input 0, we have a large control effort at the beginning of the transient of the input given at 3 s, so the peak can be computed with the initial value theorem using a step input of two times the doublet amplitude

## Slide 16: Closed-Loop Analysis
Now it’s possible to create a full closed loop and tune the controllers with sintesys.
Through hinfstruct function we can tune the free parameters of the closed loop model to minimize its norm.

## Slide 17: Closed-Loop Analysis – Nominal Time Response
Retrive the different functions 
Plot the step response and compare it to the desired one
Verify control effort limitation

## Slide 18: Closed-Loop Analysis – Nominal Performance
Sensitivity function and the performance weight can be plotted to verify nominal performance

## Slide 19: Closed-Loop Analysis – Control Effort
Same can be done for the control sensitivity function

## Slide 20: Closed-Loop Analysis – Stability Margins
Margins of Loop transfer function are shown
This margins are very good for both the gain and the phase

## Slide 21: Robust Stability
To verify robust stability, we first express our uncertain system in M-Delta form.
For robust stability we need to verify that M is asymptotically stable and that its maximum singular value is less than one for every frequency.

## Slide 22: Robust Stability
Check on the poles of M, because neccesary condition for the stability of is that it must not have positive poles
Plotting poles of M we can observe that all of them are with negative real part, so M internal stability is satisfied

## Slide 23: Robust Stability
Since our delta matrix is not full but diagonal, we can use D scaling: we use fsolve to find the diagonal D matrix that minimizes the maximum singular value
We can observe a very low maximum singular value, coherent with our very high stability margins

## Slide 24: Robust Performance
From "S. Skogestad, I. Postlethwaite, Multivariable Feedback Control Analysis and Design" we know that robust performance is equivalent to the robust stability of our system with a perturbation.
Having expressed our perturbed system in M-delta form we perform the steps outlined previously

## Slide 25: Robust Performance
Again we must check the poles of M, because neccesary condition for the stability of is that it must not have positive poles
Plotting poles of M we can observe that all of them are with negative real part, so M internal stability is satisfied

## Slide 26: Robust Performance
We observe a maximum singular value less than one, thus robust performance is verified for our system.

## Slide 27: Robust Performance – Additional Analisys

## Slide 28: Montecarlo Analysis
To correctly run the Montecarlo Analysis was crucial to have gaussian distribution for the uncertainties, which is obtained with normrnd
A struct with the new values of the system parameters is created and substitued in the system with usubs, this result as a better option than create the matrixes at every step, from a computational view point
Complementary sensitivity function and control sensitivity function are retrived to compute nominal performance and control effort

## Slide 29: Montecarlo Analysis – Nominal Performance
We notice that the settling time converges fairly quickly and from the histogram we see that all the values fall below the target treshold

## Slide 30: Montecarlo Analysis – Nominal Performance
We observe the same for the maximum control effort.
In this case the threshold is even outside the picture

## Slide 31: Montecarlo Analysis
Overshoot convergence is not smooth as the others because most of the vaues are zero and the few non-zero values cause spikes
Overshoot is expected to be below the target 99.7% of the cases with a 99.9% confidence

## Slide 32: Conclusions
END
Thank you for the attention
We obtained succesfully a controller for the lateral dynamics which allows the closed-loop system to meet all the requirements
We proved that stability and performance are robust with respect to uncertainties
We verified the validity of our analysis with montecarlo simulations